## Slide 1: HP AutoRAID (Lecture 5, cs262a)
Ion Stoica,
UC Berkeley
September 13, 2016
(based on presentation from John Kubiatowicz, UC Berkeley)
Notes: 3-D graph
Checklist
What we want to enable
What we have today
How we’ll get there

## Slide 2: Array Reliability
Reliability of N disks = Reliability of 1 Disk ÷ N
  50,000 Hours ÷ 70 disks = 700 hours
Disk system MTTF: Drops from 6 years to 1 month!
Arrays (without redundancy) too unreliable to be useful!
Hot spares support reconstruction in parallel with
access: very high media availability can be achieved

## Slide 3: RAID Basics: Levels* of RAID
RAID 0: striping with no parity (just bandwidth)
  High read/write throughput; theoretically Nx where N is number of disks
  No data redundancy
Levels in RED are used in practice
https://en.wikipedia.org/wiki/Standard_RAID_levels

## Slide 4: RAID Basics: Levels* of RAID
RAID 0: striping with no parity (just bandwidth)
RAID 1: Mirroring, simple, fast, but 2x storage
  Each disk is fully duplicated onto its "shadow”  high availability
  Read throughput (2x) assuming N disks
  Writes (1x): two physical writes
Levels in RED are used in practice
https://en.wikipedia.org/wiki/Standard_RAID_levels

## Slide 5: RAID Basics: Levels* of RAID
RAID 2: bit-level interleaving with Hamming error-correcting codes
  d bit Hamming code can detect d-1 errors and correct (d-1)/2
  Need synchronized disks, i.e., spin at same angular rotation
Levels in RED are used in practice
https://en.wikipedia.org/wiki/Standard_RAID_levels
Hamming code

## Slide 6: RAID Basics: Levels* of RAID
RAID 3: byte-level striping with dedicated parity disk
  Dedicated parity disk is write bottleneck: every write writes parity
Levels in RED are used in practice
https://en.wikipedia.org/wiki/Standard_RAID_levels
parity disk

## Slide 7: RAID Basics: Levels* of RAID
RAID 4: block-level striping with dedicated parity disk
  Same bottleneck problems as RAID 3
Levels in RED are used in practice
https://en.wikipedia.org/wiki/Standard_RAID_levels
parity disk

## Slide 8: RAID Basics: Levels* of RAID
RAID 5: block-level striping with rotating parity disk
  Most popular; spreads out parity load; space 1-1/N, read/write (N-1)x
Levels in RED are used in practice
https://en.wikipedia.org/wiki/Standard_RAID_levels
parity block

## Slide 9: RAID Basics: Levels* of RAID
RAID 5: block-level striping with rotating parity disk
  Most popular; spreads out parity load; space 1-1/N, read/write (N-1)x
RAID 6: RAID 5 with two parity blocks (tolerates two drive failures)
  Use with today’s drive sizes! Why?
    Correlated drive failures (2x expected in 10hr recovery) [Schroeder and Gibson, FAST07]
    Failures during multi-hour/day rebuild in high-stress environments
Levels in RED are used in practice

## Slide 10: Redundant Arrays of Disks RAID 5+: High I/O Rate Parity
D0
D1
D2
D3
P
D4
D5
D6
P
D7
D8
D9
P
D10
D11
D12
P
D13
D14
D15
P
D16
D17
D18
D19
D20
D21
D22
D23
P
Disk Columns
Increasing
Logical
Disk
Addresses
Stripe
Stripe
Unit
Targeted for mixed
applications
…
…
…
…
…
Independent writes possible because of interleaved parity
Reed-Solomon Codes ("Q") for protection during reconstruction
A logical write becomes four physical I/Os

## Slide 11: Problems of Disk Arrays: Small Writes
D0
D1
D2
D3
P
D0'
D0'
D1
D2
D3
P'
+
old
data
XOR
(1. Read)
+
old
parity
XOR
(2. Read)
new
data
(3. Write)
(4. Write)
RAID-5: Small Write Algorithm
1 Logical Write = 2 Physical Reads + 2 Physical Writes

## Slide 12: System Availability: Orthogonal RAIDs
Array
Controller
String
Controller
. . .
String
Controller
String
Controller
String
Controller
String
Controller
String
Controller
. . .
. . .
. . .
. . .
. . .
Redundant Support Components: fans, power supplies, controller, cables
Data Recovery Group: unit of data redundancy
End to End Data Integrity: internal parity protected data paths

## Slide 13: System-Level Availability
I/O Controller
Array Controller
. . .
. . .
. . .
Array Controller
. . .
. . .
.
.
.
Recovery
Group
Goal: No Single
Points of
Failure
host
Fully dual redundant
I/O Controller
host
with duplicated paths, higher performance can be
obtained when there are no failures

## Slide 14: HP AutoRAID – Motivation
Goals: automate the efficient replication of data in a RAID
  RAIDs are hard to setup and optimize
  Different RAID Levels provide different tradeoffs
  Automate the migration between levels
RAID 1 and 5: what are the tradeoffs?
  RAID 1: excellent read performance, good write performance, performs well under failures, expensive
  RAID 5: cost effective, good read performance, bad write performance, expensive recovery

## Slide 15: HP AutoRAID – Motivation
Each kind of replication has a narrow range of workloads for which it is best...
  Mistake ⇒ 1) poor performance, 2) changing layout is expensive and error prone
  Difficult to add storage: new disk ⇒ change layout and rearrange data...
  Difficult to add disks of different sizes

## Slide 16: HP AutoRAID – Key Ideas
Key idea: mirror active data (hot), RAID 5 for cold data
  Assumes only part of data in active use at one time
  Working set changes slowly (to allow migration)

## Slide 17: HP AutoRAID – Key Ideas
How to implement this idea?
  Sys-admin
    make a human move around the files.... BAD. painful and error prone
  File system
    Hard to implement/ deploy; can’t work with existing systems
  Smart array controller: (magic disk) block-level device interface
    Easy to deploy because there is a well-defined abstraction
    Enables easy use of NVRAM (why?)

## Slide 18: AutoRAID Details
PEX (Physical Extent): 1MB chunk of disk space
PEG (Physical Extent Group): Size depends on # Disks
  A group of PEXes assigned to one storage class
Stripe: Size depends # Disks
  One row of parity and data segments in a RAID 5 storage class
Segment: 128 KB
  Strip unit (RAID 5) or half of a mirroring unit
Relocation Block (RB): 64KB
  Client visible space unit

## Slide 19: Closer Look

## Slide 20: Putting Everything Together
Virtual Device Tables
  Map RBs to PEGs
  RB allocated to a PEG only when written
PEG Tables
  Map PEGs to physical disk addresses
  Unused slots in PEG are marked free until and RB is allocated to them

## Slide 21: HP AutoRaid – Features
Promote/demote in 64K chunks (8-16 blocks)
  Hot swap disks, etc. (A hot swap is just a controlled failure.)
  Add storage easily (goes into the mirror pool)
  Useful to allow different size disks (why?)
No need for an active hot spare (per se);
  Just keep enough working space around
Log-structured RAID 5 writes
  Nice big streams, no need to read old parity for partial writes

## Slide 22: Questions
When to demote? When there is too much mirrored storage (>10%)
  Demotion leaves a hole (64KB). What happens to it? Moved to free list and reuse
  Demoted RBs are written to the RAID5 log, one write for data, a second for parity
Why log RAID 5 better than update in place?
  Update of data requires reading all the old data to recalculate parity
  Log ignores old data (which becomes garbage) and writes only new data/parity stripes
How to promote? When a RAID5 block is written...
  Just write it to mirrored and the old version becomes garbage.

## Slide 23: Questions
How big should an RB be?
  Bigger ⇒ Less mapping information, fewer seeks
  Smaller ⇒ fine grained mapping information
How do you find where an RB is?
  Convert addresses to (LUN, offset) and then lookup RB in a table from this pair
  Map size = Number of RBs and must be proportional to size of total storage
How to handle thrashing (too much active write data)?
  Automatically revert to directly writing RBs to RAID 5!

## Slide 24: Issues
Disks writes go to two disks (since newly written data is “hot”).
  Must wait for both to complete - why?
  Does the host have to wait for both? No, just for NVRAM
Controller uses cache for reads
Controller uses NVRAM for fast commit, then moves data to disks
  What if NVRAM is full? Block until NVRAM flushed to disk, then write to NVRAM

## Slide 25: Issues
What happens in the background?
  1) compaction, 2) migration, 3) balancing
Compaction: clean RAID 5 and plug holes in the mirrored disks
  Do mirrored disks get cleaned? Yes, when a PEG is needed for RAID5; i.e., pick a disks with lots of holes and move its used RBs to other disks Resulting empty PEG is now usable by RAID5
  What if there aren’t enough holes? Write the excess RBs to RAID5, then reclaim the PEG
Migration: which RBs to demote? Least-recently-written (not LRU)
Balancing: make sure data evenly spread across the disks. (Most important when you add a new disk)